## Slide 1: 802.11
tricks & treats by @090h

## Slide 2: 802.11 basics

## Slide 3: __init__
Created by: NCR Corporation/AT&T
Invention: 1991 (Wave LAN)
Father: Vic Hayes
Name: taken from Hi-Fi
Frequency: 2.4GHz UHF and 5GHz SHF
Public release: 1997
Maximum speed: 2Mbit/s

## Slide 4: 802.11 legacy
Date: June 1997
Frequency: 2.4 GHz
Bandwidth: 22 MHz
Modulation: DSSS, FHSS
Data rate: 1, 2 Mbit/s
Range indoor: 20m
Range outdoor: 100m

## Slide 5: 802.11a
Date: September 1999
Frequency: 5, 3.7 GHz
Modulation: OFDM
Bandwidth: 20 MHz
Speed: 6, 9, 12, 18, 24, 36, 48, 54 Mbit/s
Range indoor: 35m
Range outdoor: 120m

## Slide 6: 802.11b
Date: September 1999
Frequency: 2.4 GHz
Modulation: DSSS
Bandwidth: 22 MHz
Speed: 1, 2, 5.5, 11 Mbit/s
Range indoor: 35m
Range outdoor: 140m

## Slide 7: 802.11g
Date: September 2003
Frequency: 2.4 GHz
Modulation: OFDM,DSSS
Bandwidth: 20 MHz
Speed: 6, 9, 12, 18, 24, 36, 48, 54 Mbit/s
Range indoor: 38m
Range outdoor: 140m

## Slide 8: 802.11n
Date: October 2009
Frequency: 2.4/5 GHz
Modulation: OFDM
Bandwidth: 20 MHz, 40 MHz
Speed in Mbit/s
[ 7.2, 14.4, 21.7, 28.9, 43.3, 57.8, 65, 72.2 ]
[ 15, 30, 45, 60, 90, 120, 135, 150 ]
Range indoor: 70m
Range outdoor: 250m
MIMO: 4x4 or SISO: 1x1

## Slide 9: 802.11ac
Date: December 2013
Frequency: 5 GHz
Modulation: OFDM
Bandwidth: 20 MHz, 40 MHz, 80 MHz, 160 MHz
Speed in Mbit/s
[ 7.2, 14.4, 21.7, 28.9, 43.3, 57.8, 65, 72.2, 86.7, 96.3 ]
[ 15, 30, 45, 60, 90, 120, 135, 150, 180, 200 ]
[ 32.5, 65, 97.5, 130, 195, 260, 292.5, 325, 390, 433.3 ]
[ 65, 130, 195, 260, 390, 520, 585, 650, 780, 866.7 ]
Range indoor: 35m Range outdoor: NO!
MIMO: 8x8 streams!

## Slide 10: 802.11 1999-2016
802.11 standard evolution |  |  |  |  | 
IEEE Standard | 802.11a | 802.11b | 802.11g | 802.11n | 802.11ac
Year Adopted | 1999 | 1999 | 2003 | 2009 | 2014
Frequency | 5 GHz | 2.4 GHz | 2.4 GHz | 2.4/5 GHz | 5 GHz
Max. Data Rate | 54 Mbps | 11 Mbps | 54 Mbps | 600 Mbps | 1 Gbps
Typical Range Indoors* | 100 ft. | 100 ft. | 125 ft. | 225 ft. | 90 ft.
Typical Range Outdoors* | 400 ft. | 450 ft. | 450 ft. | 825 ft. | 1,000 ft.

## Slide 11: Nearest future

## Slide 12: 802.11 SPEED² EVOLUTION

## Slide 16: SISO/SIMO/MISO/MIMO

## Slide 17: WTF is MIMO?

## Slide 18: MIMO vs MU-MIMO

## Slide 19: Channels and plans

## Slide 20: 802.11b channels

## Slide 21: 2.4GHz channel plan world

## Slide 22: 2.4GHz channel plan US

## Slide 23: Channel plans
US: 1 – 6 – 11
JP: 1 – 5 – 9 – 13 – 14 for 802.11b
WORLD: 1 – 5 – 9 – 13

## Slide 24: IRL mistakes that killed 2.4GHz
WTF is channel plan?
More bandwidth  more speed
More power  more speed

## Slide 25: Home Wi-Fi tweaks
Use ACS or set channel to most free (11 usually)
Use 40MHz wisely
Lower TX power if possible

## Slide 26: 5GHz channels

## Slide 27: 5GHz WORLD WIDE

## Slide 28: Country  RF limits  CRDA
Allowed almost everywhere:
Channels: 1- 11
Signal strength (20dBm = 100mW)
Omnidirectional antenna (6dBi)

## Slide 29: Free channel?
Уровень на входе приемника выше уровня среднего шума
На входе приемника есть реальный сигнал
Комбинированный = 1 + 2
Получение реального сигнала за фиксированный промежуток времени
Комбинированный = 1 + 4
Уровень на входе приемника выше уровня -82dBm, но меньше -62dBm. + канал занят, если уровень больше -72dBm и можно декодировать сигнал
https://wireless.wiki.kernel.org/en/users/documentation/acs

## Slide 30: 802.11 XXX

## Slide 31: 802.11 timeline

## Slide 32: 802.11i
Security mechanisms for 802.11
Auth, crypto
Draft: 24 June 2004
Released: IEEE 802.11-2007
P.S. China has WAPI https://en.wikipedia.org/wiki/WLAN_Authentication_and_Privacy_Infrastructure

## Slide 33: 802.11e
Wi-Fi Multimedia (WMM), Wireless Multimedia Extensions (WME)
QoS for 802.11

## Slide 34: 802.11d
802.11d - is an amendment to the IEEE 802.11 specification that adds support for "additional regulatory domains".
Used to regulate:
Channelization
Hopping patterns
As of January 1, 2015, the U.S. Federal Communications Commission banned the use of 802.11d within the U.S.

## Slide 35: 802.11d

## Slide 36: 802.11d in the wild

## Slide 37: 802.11d OSX fix
http://www.hub.ru/wiki/802.11d
https://github.com/0x90/osx-scripts/blob/master/wifi_cc.sh

## Slide 38: 2.4GHz, 5GHz? …8(
802.11 frequency ranges:
900 MHz (802.11ah)
2.4 GHz (802.11b/g/n)
3.6 GHz (802.11y)
4.9 GHz (802.11y) Public Safety WLAN
5 GHz (802.11a/h/j/n/ac)
5.9 GHz (802.11p)
60 GHz (802.11ad)

## Slide 39: 802.11y
3.65-3.7GHz, 54Mbit/s, 4.9 GHz. US only? Public Safety WLAN 50 MHz of spectrum from 4940 MHz to 4990 MHz (WLAN channels 20–26) are in use by public safety entities in the US. Cisco 3202 4.9GHz Wireless Mobile Interface Card

## Slide 40: 802.11p
5.9Ghz, Wireless Access in Vehicular Environments (WAVE) 802.11p In Europe used as a basis for the ITS-G5 standard, supporting the GeoNetworking vehicle2vehicle2infrastructure communication.
Intellectual Transport System. =^.^=

## Slide 41: 802.11ad
60 GHz,WiGig. 7Gbit/s, 10m, beamforming, wireless display/HDMI, uncompressed video

## Slide 42: 802.11ah
900 MHz operates in sub-gigahertz unlicensed bands.

## Slide 43: 802.11s = mesh

## Slide 44: …and many more

## Slide 45: ANTENNA

## Slide 46
=
+
?

## Slide 47: Основные характеристики антенн

## Slide 48: Основные Виды антенн в сетях WiFI
Штыревые / всенаправленные – спиральные
Волновой канал – Уда-Яги
Панельные – патч-антенны
Параболические – зеркальные
Секторные – волноводно-щелевые

## Slide 49: Спиральные антенны

## Slide 50: Спиральные антенны

## Slide 51: Волновой канал

## Slide 52: Волновой канал

## Slide 53: Патч антенны

## Slide 54: Патч антенны

## Slide 55: Зеркальные Антенны

## Slide 56: Зеркальные Антенны

## Slide 57: Волноводно-щелевые Антенны

## Slide 58: Волноводно-щелевые Антенны

## Slide 61: HARDWARE

## Slide 62: .:MODES:.
STA/Managed– station operating
AP/Master – access point
MON – passive monitor channel
INJMON – monitor+injection (mac80211)
AdHoc/IBSS – computers without AP
WDS – static WDS
Mesh – many to many

## Slide 63: CARDS
TP-Link TL-WN722N Atheros AR9271 (2.4 GHz)
Alfa AWUS036H RTL8187L (2.4 GHz)
Alfa AWUS036NHA (2.4G GHz) long range
Alfa AWUS051NH (2.4 & 5 GHz) long range
Ralink 3070 based cards (MediaTek now)
Any MAC80211 can be used!

## Slide 64: MAX POWER DREAMS?

## Slide 65: GOOD OLD TYMES….GO TO BOLIVIA!

## Slide 66: HACKER = NO LIMITS
# ifconfig wlan0 down
# iw reg set BO BZ
# ifconfig wlan0 up
# iwconfig wlan0 channel 13
# iwconfig wlan0 txpower 30
or
# iw phy wlan0 set txpower fixed 30mBm

## Slide 67: Correct way
Patch wireless-database
Patch CRDA
PROFIT!!!!
https://github.com/0x90/kali-scripts/blob/master/wireless.sh

## Slide 68: 802.11 OSI

## Slide 69: 802.11 layer in OSI

## Slide 71: 802.11 modulation

## Slide 72: DSSS
DSSS (direct sequence spread spectrum) - метод прямой последовательности для расширения спектра

## Slide 73: DSSS

## Slide 74: OFDM
OFDM (англ. Orthogonal frequency-division multiplexing — мультиплексирование с ортогональным частотным разделением каналов) является цифровой схемой модуляции, которая использует большое количество близко расположенных ортогональных поднесущих.
Wi-Fi, WiMax, LTE

## Slide 75: OFDM

## Slide 76: DSSS vs OFDM

## Slide 77: 802.11 data rates

## Slide 78: Physical layer
802.11a: OFDM - Мультиплексирование с ортогональным частотным разделением каналов
802.11b: DSSS - Расширение спектра методом прямой последовательности
802.11g: Extended Rate PHY (ERP) = OFDM
802.11n: MIMO OFDM
802.11ac: MU MIMO OFDM

## Slide 79: 802.11 security

## Slide 80: 802.11 SECURITY
Open
WEP
IBSS aka Ad-Hoc
WPA
WPA2-Personal
WPA2-Enterprise

## Slide 81: management frame types
Authentication frame
Deauthentication frame
Association request frame
Association response frame
Disassociation frame
Beacon frame
Probe request frame
Probe response frame

## Slide 82: WiFi passive scan

## Slide 83: WiFi active scan

## Slide 84: WiFi open auth

## Slide 85: WiFi PSK auth

## Slide 86: 802.11 connection

## Slide 87: WEP/WPA/WPA2

## Slide 88: WiFi authentication types
Open Authentication to the Access Point
Shared Key Authentication to the Access Point
EAP Authentication to the Network
MAC Address Authentication to the Network
Combining MAC-Based, EAP, and Open Authentication
Using CCKM for Authenticated Clients
Using WPA Key Management
http://www.cisco.com/c/en/us/td/docs/routers/access/wireless/software/guide/SecurityAuthenticationTypes.html

## Slide 89: HACKING

## Slide 90: What to hack?
WiFi network (AP)
WiFi clients
Almost like fishing and XSS.
Active and passive.
May be combined.

## Slide 91: TOOLS
wifite r112
kismet, horst, aircrack-ng, mdk3, wifijammer
pyrit, cowpatty, hashcat
KARMA, MANA, Hostapd-WPE
reaver, pixie-wps, WPSPIN.sh, BullyWPS,
FruityWiFi, Snoopy-ng, modwifi
scapy + impacket + /dev/brain + /dev/hands

## Slide 92: RFMON
Like promiscuous mode but at lower layer
Used to receive ALL frames
Used for sniff and injection
Advice: don’t kill network-manager – free the card
# airmon-ng start wlan0
# airodump-ng wlan0mon
… may be use wireshark?

## Slide 93: Radiotap
Radiotap is a de facto standard for 802.11 frame injection and reception.
Radiotap is pseudo layer
http://www.radiotap.org/

## Slide 94: WEP HACKING

## Slide 95: WEP
WEP = Wired Equivalent Privacy
First WiFi crypto
WEP = RC4 + CRC32 + XOR
LENGTH(KEY) = 40 (1997)
LENGTH(KEY) = 104 (2001)
Has many bugs
Can be hacked in 10 minutes
Almost dead. Deprecated since 2004.

## Slide 96: WEP weakness
HACK RC4 = HACK WEP
SMALL IV (init vector) = HACK
CRC weakness
NO AUTH, ONLY CRYPTO!

## Slide 97: Атака на WEP
Направленная антенна => собираем IV с точки доступа
Антенна с широкой диаграммой => точка доступа + клиенты

## Slide 98: WPA/WPA2 HACKING

## Slide 99: WPA/WPA2 handshake catching
1. Пассивный режим:
Секторная антенна или всенаправленная антенна, желательно карта с MIMO
2. Активный режим:
Две сетевых карты: Одна мощная карта с направленной антенной для deauth, вторая карта с секторной антенной для перехвата в пассивном режиме.

## Slide 100: HANDSHAKE CATCHING
Airodump-ng capture:
airodump-ng -c 9 --bssid 00:14:6C:7E:40:80 -w output.cap --showack wlan1mon
Pyrit capture and strip:
pyrit -r wlan1mon -o $(date +%Y-%m-%d_%H:%M:%S)_stripped.cap stripLive

## Slide 101: DEAUTH TO HELP
aireplay-ng -1 0 -e teddy -a 00:14:6C:7E:40:80 -h 00:0F:B5:88:AC:82 mon0
aireplay-ng -1 6000 -o 1 -q 10 -e teddy -a 00:14:6C:7E:40:80 -h 00:0F:B5:88:AC:82 mon0
Wifijammer.py is the best solution from the box for deauth. Launched on separate card in practice.

## Slide 102: HANDSHAKE BRUTEFORCE
Hashcat
Pyrit
Cowpatty
Cloudcracker

## Slide 103: WPA/WPA2 hacking protections?
SSID hidden
802.11w
IDS solutions arriving

## Slide 104: HALF HANDSHAKE STORY

## Slide 105: Questions
Do we REALY need all 4 frames for handshake cracking?
What will happen if the client will try to connect to the same SSID with wrong password?

## Slide 106: BAD/HALF HANDSHAKE

## Slide 107: HALF HANDSHAKE TOOLS
Pyrit --all-handshakes : Use all handshakes instead of the best one
https://github.com/dxa4481/WPA2-HalfHandshake-Crack
halfHandshake.py -r sampleHalfHandshake.cap -m 48d224f0d128 -s SSID_HERE

## Slide 108: PoC thoughts
Make custom HostAP fork
Combine MANA and password auth with random password
Write own access point from scratch

## Slide 109: Lame PoC
Hardware: TP-Link 3020/3040/3220/..
Firmware: Custom OpenWRT based
http://semaraks.blogspot.ru/2014/12/wispi-ver-11-for-tp-link-mr3020-mini.html
Attack: KARMA + Randoom password @ hostapd.conf
Cracking: pyrit --all-handshakes

## Slide 110: ADVANCED FUTURE
Hardware: Atheros chips
Software: Python + Scapy + FakeAP + WiFi MAP database
Cracking: pyrit --all-handshakes
PWNiNiNG: setting different password for different client based on SSID database + MiTM attacks

## Slide 111: WPS HACKING

## Slide 112: WPS
WPS – wireless protected setup
Designed for connecting printers and other embedded devices
Used by hackers to easily hack Wi-Fi

## Slide 113: WPS HACKING WAYS
WPS PIN brute force
WPS PIN generation
WPS PIN guessing

## Slide 114: WPS BRUTE ALGO
If the WPS Registration Protocol fails at some point, the Registrar will send a NACK message.
If the attacker receives a NACK message after sending M4, he knows that the first half of the PIN was incorrect. See definition of R-Hash1 and R-Hash2.
If the attacker receives a NACK message after sending M6, he knows that the second half of the PIN was incorrect.

## Slide 115: WPS PIN brute force
How many to brute? 8? 7? 4+3=>10^4+10^3
Направленная антенна + подбор тракта по мощности
Wifite, reaver-wps, bully, BullyWPSRussian.sh, ReVdK3-r2.sh

## Slide 116: WPS PIN generation
WPS_PIN=SOME_ALGO(MAC_ADDRESS)
PIN = RAND(SERIAL) is not really random too
Serial disclosure in Beacon frames at vendor specific fields
Vulnerable vendors: ZyXELL, D-Link, Belkin, Huawei
Reaver -W, --generate-pin Default Pin Generator [1] Belkin [2] D-Link [3] Zyxel
Different custom pin generators https://github.com/devttys0/wps

## Slide 117: PIXIE WPS/PIXIE DUST
"pixie dust attack" discovered by Dominique Bongard in summer 2014
Weak PRNG
Pixiewps for _OFFLINE_ brute force

## Slide 118: PIN GUESS
Good PRNG @ embedded devices is a problem. E-S1 and E-S2 need to be random.
NONCE = RAND(MAC) is not really random
NONCE = RAND(time=01.01.1970 by default) is no really random too
Vendors: Realtek, Ralink, Broadcom, MediaTek
Tools: wifite fork, Pixiewps, reaver t6x fork

## Slide 119: Protections?
WPS activation for 1 minute after BUTTON pressed (mgts)
PIN from the end: 9999****
WPS brute force timeout
WPS brute force ban by MAC

## Slide 120: WPA ENTERPRISE HACKING

## Slide 121: WPA-Enterprise

## Slide 122: EAP,EAPOL/EAPOR

## Slide 123: WiFi + EAP
EAP-TLS
EAP-MD5
EAP-SIM
EAP-AKA
PEAP
LEAP
EAP-TTLS
http://en.wikipedia.org/wiki/Extensible_Authentication_Protocol

## Slide 124: PASSIVE Wi Fi HACKING

## Slide 126: Abbreviations part 1
SSID – Service Set Identifiers (ESSID)
BSSID – Basic service set identification (AP MAC)
RSSI – Received Signal Strength Indication
CINR – Carrier to Interference + Noise Ratio
ACS – Auto Channel Selection
WEP – Wired Equivalent Privacy
WPA – Wi-Fi Protected Access aka Robust Secure Network (RSN)

## Slide 127: Abbreviations part 2
AES – Advanced Encryption Standard
TKIP – Temporal Key Integrity Protocol
CCMP – Counter Mode with Cipher Block Chaining Message Authentication Code Protocol
EAP – Extensible Authentication Protocol
LEAP – Lightweight Extensible Authentication Protocol
RADIUS – Remote Authentication Dial In User Service

## Slide 128: Abbreviations part 3
WPS/QSS – Wireless protected setup. WPS PIN  WiFi Password
PSK – Pre-Shared Key
MIC – Michael message integrity code
Authentication, Authorization, and Accounting (AAA) Key - Key information that is jointly negotiated between the Supplicant and the Authentication Server (AS). This key information is transported via a secure channel from the AS to the Authenticator. The pairwise master key (PMK) may be derived from the AAA key.
Pairwise Master Key (PMK) – The highest order key used within the 802.11i amendment. The PMK may be derived from an Extensible Authentication Protocol (EAP) method or may be obtained directly from a Preshared key (PSK).
Pairwise Transient Key (PTK) - A value that is derived from the pairwise master key (PMK), Authenticator address (AA), Supplicant address (SPA), Authenticator nonce (ANonce), and Supplicant nonce (SNonce) using the pseudo-random function (PRF) and that is split up into as many as five keys, i.e., temporal encryption key, two temporal message integrity code (MIC) keys, EAPOL-Key encryption key (KEK), EAPOL-Key confirmation key (KCK).
Group Master Key (GMK) - An auxiliary key that may be used to derive a group temporal key (GTK).
Group Temporal Key (GTK) - A random value, assigned by the broadcast/multicast source, which is used to protect broadcast/multicast medium access control (MAC) protocol data units (MPDUs) from that source. The GTK may be derived from a group master key (GMK).

## Slide 129: BOOKS
802.11 Wireless Networks The Definitive Guide - Matthew Gast
802.11n A Survival Guide – Matthew Gast
Стандарты 802.11

## Slide 130: Links
https://en.wikipedia.org/wiki/IEEE_802.11

## Slide 131: My repos
https://github.com/0x90/kali-scripts
https://github.com/0x90/wifi-arsenal
https://github.com/0x90/wifi-scripts
https://github.com/0x90/esp-arsenal

## Slide 132: 802.11 pwner in real life